## Slide 1
华东师范大学 软件工程学院
肖波
数学馆 215
Email: bxiao@sei.ecnu.edu.cn
Advanced Computer Networks
高级计算机网络

## Slide 2
Introduction
引言
Chapter 1

## Slide 3: Internet structure: network of networks
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
access
net
…
…
…
…
…
…
ISP B
ISP A
ISP C
IXP
IXP
regional net

## Slide 4: 多样化的网络形态
互联网
无线网络
移动通信网
卫星网
物联网
数据中心网络
专用网络
……
智慧城市
信息物理融合系统（CPS）
嵌入式网络计算
雾计算、边缘计算
工业4.0、智能制造
5G、6G …

## Slide 5: What’s the Internet
millions of connected computing devices:
  hosts = end systems
  running network apps
communication links
  fiber, copper, radio, satellite
  transmission rate: bandwidth
Packet switches: forward packets (chunks of data)
  routers and switches
wired
links
wireless
links
router
mobile network
global ISP
regional ISP
home
network
institutional
network
smartphone
PC
server
wireless
laptop
Notes: 5

## Slide 6
Internet: “network of networks”
  Interconnected ISPs
protocols control sending, receiving of msgs
  e.g., TCP, IP, HTTP, Skype, 802.11
Internet standards
  RFC: Request for comments
  IETF: Internet Engineering Task Force
What’s the Internet
mobile network
global ISP
regional ISP
home
network
institutional
network

## Slide 7
a human protocol and a computer network protocol:
Q: other human protocols?
Hi
Hi
Got the
time?
2:00
TCP connection
response
Get http://www.awl.com/kurose-ross
<file>
time
TCP connection
request
What’s a protocol? 协议

## Slide 8: 基本概念
网络体系结构
  完成计算机间的通信合作，把每个计算机互联的功能划分成有明确定义的层次，并规定同层次进程通信的协议及相邻层之间的接口服务
协议（Protocol）
  协议就是为实现网络中的数据交换建立的规则标准或约定。协议由语法、语义和交换规则三部分组成，即协议的三要素。

## Slide 9
接口(Interface)
  分层结构中各相邻层之间要有一个接口，它定义了较低层向较高层提供的原始操作和服务。相邻层通过它们之间的接口交换信息，高层并不需要知道低层是如何实现的，仅需要知道该层通过层间的接口所提供的服务，这样使得两层之间保持了功能的独立性。

## Slide 10: 网络协议层次
Layers, protocols, and interfaces.

## Slide 11: 协议层次
Example information flow supporting virtual communication in layer 5.

## Slide 12: Connection-Oriented and Connectionless Services(2)
Six different types of service.

## Slide 13: Reference Models
The OSI reference model.

## Slide 14: Reference Models (2)
The TCP/IP reference model.

## Slide 15: Hybrid Model
The hybrid reference model to be used in this book.

## Slide 16: 封装 Encapsulation
source
application
transport
network
link
physical
Ht
Hn
M
segment
Ht
datagram
destination
application
transport
network
link
physical
Ht
Hn
Hl
M
Ht
Hn
M
Ht
M
M
network
link
physical
link
physical
Ht
Hn
Hl
M
Ht
Hn
M
Ht
Hn
M
Ht
Hn
Hl
M
router
switch
message
M
Ht
M
Hn
frame

## Slide 17: Architecture of the Internet
Overview of the Internet.

## Slide 18: IEEE 802 Standards
The 802 working groups. The important ones are marked with *. The ones marked with  are hibernating. The one marked with † gave up.